Disparity for Stereo Vision

Project illustrated by Thomas Bong

50126179

CSE473 Image Processing

Project Submitted Date : December 16th, Friday 2016

Disparity for Stereo Vision project consists of two main components; 1) Block matching for disparity 2) Dynamic Programming to construct a disparity map. Both components’ purpose is to extract the depth information of real objects within the given images that were taken from two different angles, left and right. Disparity consists of the information about depth(displacement) of the objects within the image by comparing the distance of a specific pixel from image 1 to the same pixel in image 2. For example, seeing only with your left eye and right eye would differ in angle of the view. That is the main concept of disparity. Disparity map by the block matching method begins with setting a block(pixels) size either 3 by 3 or 9 by 9 and search for the same pixel values by calculating the SSD(Sum of Squared Differences) of the two blocks within a fixed-size search distance. The search distance will be discussed later. Dynamic Programming is similar to calculating the longest common subsequence of the pixel values within a fixed-size search distance. More detailed explanation on the methods will be thoroughly presented later. The concepts that were covered in class include stereo imaging with base line, disparity and multi-camera imaging. Multi-camera imaging is not specifically mentioned in the project description, but the 2 given images are the examples of multi-camera imaging. The two images were taken from 2 different angles, giving more information about the displacement of objects within the image. The main purpose of the project was to construct disparity maps by using the block matching algorithm with a variety of block sizes or with dynamic programming.
As mentioned above, block matching with 3x3 and 9x9 uses a block of pixels from the input image to the target image. Block matching was first processed as it was simpler than the dynamic programming approach. First, a block of 3 pixels by 3 pixels from the left image is initially set at index (1,1) and end at (last row-1, last column -1). For block matching with 3x3 block skips first row, first column, last row and last column because as the block is 3x3, if the row or column value is 0 or the last index, then the block size cannot be 3x3. The same principle applies to 9x9, the only difference is the first and last 4 rows and columns will be skipped as 9x9 would be able to start at (4,4) and end at (last row -4, last column-4). Then, a search distance is set. Search distance defines how many pixels to the right(because I’ve decided to compare pixels from the left image to the right image) I will be comparing the the 3x3 block from the left image with the 3x3 block from the right image. Initial search distance was 50 pixels. The range of search distance affects the results because if the search distance is too short, then you may not be reaching the same pixel. If the search distance is too long, it would not be the optimal solution to the problem in terms of time, because you may have already passed the specific pixel that you were looking for, then the program may be slightly wasting time doing unnecessary calculations. After setting the search distance, for each iteration of the right image, new block gets created, and is compared with the initial block from the left image. The comparison is proceeded by calculating the SSD value. Each pixel from the right image block is subtracted from the same index pixel from the left image and then the subtracted value is squared. The sum of all the ‘squared differences’ is the SSD. SSD value represents the similarity of the two blocks. The less the SSD, the more identical the two blocks are. When the similar/identical block is found, x-axis(column) distance from the left image pixel to the right image pixel is calculated by subtracting the current pixel column index(j) of the left image and the current column index(j) of the right image, then the distance value represents the disparity of the two pixels. The two images were rectified beforehand, therefore I only needed to compare the x-axis difference. The disparity value for each pixel was appended to the disparity image array. 9X9 block matching was processed exactly the same way with a different block size mentioned above. As you may see below, disparity images differ by both SSD and search distance. Different results with different SSD values will be presented later.
Similarly, dynamic programming algorithm’s purpose is to construct a disparity map, but with a different method. Dynamic programming approach looks at each row from the left and right image. For 20 pixels(search distance) from each left and right image is compared and the longest common subsequence is calculated within the 20 pixels. The reason why only 20 pixels from each of the left and right image are compared rather than the whole row is because we are looking for the disparity of objects from the two images. For example, if an object exists in (0,4) in the left image, then the object would exist somewhere in (0, 10) or (0,20) in the right image. The column distance of the object from the left image and the right image would not be very far. This is the reason why the search distance is 20, just like block matching.
To implement the program for this project, I’ve used Python. On Python, there were a few libraries that improved the quality of the process of the project. The main libraries that were used for this project were Numpy and OpenCV. Numpy arrays were used to represent the images in arrays of pixels and OpenCV’s functions such as imread() and imshow() were used in order to load/display the images. Other than the two libraries, ‘math’ was used for calculating the SSD(involving calculations with exponents). Block Matching algorithm was done manually and also, dynamic programming was done manually. However, there were a few references that guided implementing the dynamic programming algorithm. All references are listed in the reference list section of the paper.
The results of the block matching are as follows;

block matching 3x3 disparity map
SSD <=50

block matching 9x9 disparity map
SSD <= 50

Compared to the given disparity images, the above results differ in image display. Block matching 3x3 and 9x9 both take about 1-2 minutes depending on the SSD value criterion. The different results for different SSD values are displayed on the next page.
Dynamic Programming result is as follows;

Dynamic Programming Disparity Map

The difference between block matching and dynamic programming is not only the approach in calculating the disparity values, but also in dynamic programming, the longest common subsequent values will have occlusions, meaning that the longest common subsequent values may result in length 6 within the distance of 10. Then 4 values are blank(occlusion). We fill up the occlusion values. In the above example, the occlusion value was set to 20. Different occlusion values will result in different images, but only in the color of the occlusions not the result itself. More examples with different occlusions are displayed later.
All three images(block matching 3x3, 9x9 and dynamic programming) differ from the given disparity images. The problem for block matching is still unsolved. As mentioned above, the closer the SSD is to 0, the more similar the two blocks are. Thus, only the pixels that had SSD value equal to 1 or 0 were considered, first. Also, for the correctness of the results, MSE(Mean Squared Error) of the result image and the two given images(disp1, disp5) was calculated for each method. The MSE calculation is as follows;

The equation states that for each pixel of the same index from image 1 and image 2 are ‘subtracted and then squared’. The MSE value is the sum of the the ‘subtracted and then squared’ values of the all the pixels from the images and then devided by the length of row *length of columns of the image. MSE value differed depending on the SSD value criterion. The results for the 3x3 with different SSD value criterion are the following;

SSD<= 1,
MSE(disp1) : 49085.83
MSE(disp5) : 49756.43

SSD <= 5,
MSE(disp1) : 115779.05
MSE(disp5) : 117037.22
You notice that the MSE increased but the image displays clearer view.

SSD <=15
MSE(disp1) : 187730.52
MSE(disp5) :189680.78

The larger the SSD value criterion gets, the larger the MSE gets. This is correct, because the lower the SSD, the more similar the two blocks are, therefore as the SSD value gets bigger, the difference between the two blocks gets larger and results in higher MSE.

The following are the results of 9x9 block matching with different SSD values and MSE.

SSD <= 1
MSE(disp1) : 23074.57
MSE(disp5) : 23229.07

SSD <= 5,
MSE(disp1) : 56277.30
MSE(disp5) : 56502.12

SSD <= 15,
MSE(disp1) : 92241.87
MSE(disp5) : 92611.23

Dynamic Programming
Occlusion value = 20
MSE(disp1): 28039.09
MSE(disp5): 27619.37

Dynamic Programming
Occlusion value = 0
MSE(disp1): 28039.09
MSE(disp5): 27619.37

As you may see, the different occlusion values give different image display, but the MSE value is the same because in this project, occlusions were excluded from the MSE calculation. MSE only included the relevant pixel values in dynamic programming.
From the results of 3x3, 9x9 block matching and dynamic programming algorithm, the lowest MSE value was from the 9x9 block with SSD <= 1. This indicates that the 9x9 block is more precise than the 3x3 block and dynamic programming approach at searching the closest matching block. The visibility of the disparity map was best displayed by the dynamic programming approach, even though 9x9 block matching resulted in the least MSE value. The difference in grayscale value of the block matching and dynamic programming is unsolved. Both approaches should result in the same grayscale value, but block matching resulted in more darker grayscale images.
This project allowed me to study disparity thoroughly. I did not understand disparity in depth when it was discussed in class in the beginning of the semester, but throughout this project, I researched a lot of materials and understood what disparity maps represent and how they can help in estimating depth of the objects from the images taken from different angles. It has been a great experience, as previous programming homework sets, working on this project although I was not able to create a successful disparity images. Python is not my strongest language nor did I know about libraries such as openCV, numpy, but throughout the semester, I’ve become more and more familiar with Python, openCV and numpy. Working on programming assignments allowed me to understand the concepts such as Gaussian operation, Laplacian operation, Region Merging(although I did not finish the project..) and Stereo Imaging in depth by writing the actual program. The only thing that I wish I could have done better in this class is being able to actually return the correct output. I was able to manage to produce the results to some extent but I wasn’t able to produce completely correct results. However, learning the concepts and the steps carried out for each concept was enough for me to begin with image processing. With the rudimentary knowledge in image processing, I look forward to learning more advanced technologies.

Reference List
-Block Matching;
http://mccormickml.com/2014/01/10/stereo-vision-tutorial-part-i/
-MSE Calculation;
http://homepages.inf.ed.ac.uk/rbf/CVonline/LOCAL_COPIES/VELDHUIZEN/node18.html
-Dynamic Programming;
http://www.geeksforgeeks.org/dynamic-programming-set-4-longest-common-subsequence/
https://piazza.com/class/iste3bbajqf1eo?cid=251